## Slide 1
“Simple” Glass Break Detector
Michael Fuhrman
10/20/20

## Slide 2: Summary
Catching the Thud Neural Network Output at high frequency envelope peaks helps to suppress false positives while risking more false negatives.
Suppressing Thuds after Shatter also brings improvement.
Need to review why the simple (Shatter After Thud) detector is missing detections, but why suppressing Thuds after Shatter brings improvement.

## Slide 3: “Simple” Glass Break Chain
overhang('up',8, 'down',10)
cmp(‘thresh’,.3)
pulse(‘time’,001)
delay(‘delay’,.001)
cmp(‘thresh’,.5)
not
pulse(‘time’, .35)
and
Declare Shatter
After Thud
ynnShatter
ynnThud
Sampled at Peak
Thud umbrella extends passed onset of Shatter to ensure capture
Thud Neural Network is sampled at high frequency peak ( a sudden jump in signal)
See next slide.
Shatter should have some extent in time
Possible small delay so shatter threshold crossing occurs after thud threshold crossing if needed
Copyright 2020 Aspinity, Inc. Proprietary and Confidential, all rights reserved

## Slide 4: Asynchronous Peak Detector for Sampling Neural Network Output
PEAK = ramp.ops.peak('atk',100, 'dec',1, 'modelVersion','PDmodelDynamic');
CMPNN = ramp.ops.cmp('thresh',.5);
AMPpt4=ramp.ideal.amp('Av',.4);
hfPeakChain = [PEAK;
ramp.ideal.pass()] > ramp.ideal.minus() > ramp.ops.cmp('thresh',0) > …
ramp.ops.pulse('time',1e-6) > AMPpt4;
peakNNChain = [hfPeakChain;
ramp.ideal.pass() > CMPNN] > ramp.logic.gate('type','and') > AMPpt4;
ynnThudAtPeaks = peakNNChain(t, [y(:,2), ynnThud]);
y(:,2)
PEAK
passthrough
minus
Ideally y(:,2) should not have its baseline subtracted. It should be the upper envelope of the high frequency channel.
cmp(‘thresh’,0)
pulse
amp(‘gain’,.4)
Pulse on rising edge as peak detector crosses signal
Multiplies Thud Neural Network Output with a 0 or 1
Detect when peak tracker overshoots signal
Copyright 2020 Aspinity, Inc. Proprietary and Confidential, all rights reserved

## Slide 5: Why Focus on Signal Peaks?
But they also occur at other times.
How to get peak detector to deliver only prominent peaks?
Copyright 2020 Aspinity, Inc. Proprietary and Confidential, all rights reserved
4kHz peaks coincide with thuds.
400Hz peaks were sometimes missed.

## Slide 6: Single NN “Scratch” Glass break
Copyright 2020 Aspinity, Inc. Proprietary and Confidential, all rights reserved
The initial glass break detector collected the amplitudes and baselines of the high and low frequency envelopes along with the zero-crossing rate. A neural network trained on labeled shatter events within 200msec of onset along with background signal levels. An overhang operator
  (Hang=ramp.ops.overhang('up’,8, 'down’,10))
applied to the neural network output filtered out events occurring over short time intervals.
TODO: How to determine overhang parameters?
146/148 149

## Slide 7: Comparison of Timing Constraints
Simple timing constraints, i.e., shatter after thud
Sophisticated timing constraints, i.e., shatter after thud, suppress thud after shatter  more TPs and FPs
119/148 112
146/148 125
Copyright 2020 Aspinity, Inc. Proprietary and Confidential, all rights reserved

## Slide 8: Results: Focus on Peaks yields fewer FPs but a few misses
Simple timing constraints, i.e., shatter after thud, thud coincides with high frequency impulse
Sophisticated timing constraints, i.e., shatter after thud, thud coincides with high frequency impulse, suppress thud after shatter
142/148 76
141/148 67
Copyright 2020 Aspinity, Inc. Proprietary and Confidential, all rights reserved

## Slide 9: The Wide Valid Thud Pulse AND Shatter Pulse
Copyright 2020 Aspinity, Inc. Proprietary and Confidential, all rights reserved
cmp('thresh',.5)
wideValidThudPulseChain
delay('delay',.05)
pulse('time’,.2)
Threshold the Thud NN
Generate a pulse
Threshold the Shatter NN
Generate a 200msec wide pulse
Delay the Shatter pulse 50msec so it doesn’t interfere with the Thud that caused it
NOT the wide pulse
AND the result with the Thud coming after Shatter to suppress those Thuds
The remaining Thuds are valid Thuds which are widened to 150msec
cmp('thresh',.5)
pulse('time',1e-6)
NOT
AND
wideValidThudPulse
NOT
pulse('thresh’,.15)
A Thud which was more than 200msec after the onset of Shatter generates a 150msec wide pulse within which Shatter onset must be detected

## Slide 10: A Valid Thud Pulse
validThudPulseChain = [THUDTHRESH > PULSE0001;
SHATTERTHRESH > ramp.ops.pulse('time',.2)> NOT] > AND > AMPpt4;
validThudPulse (declareThud)
cmp('thresh',.5)
pulse('time',1e-6)
cmp('thresh',.5)
pulse('time’,.2)
NOT
AND
amp('Av',.4
ynnThud
ynnShatter
Suppress Thuds within 200msec of the onset of Shatter

## Slide 11: Shatter with some extent over time
Copyright 2020 Aspinity, Inc. Proprietary and Confidential, all rights reserved
ShatterPulseChain = SHATTERTHRESH > ramp.ops.overhang('up',1.25/UpTime, 'down',1.25/DownTime) > CMPpt5 > PULSE0001;
cmp('thresh',.5)
overhang('up',125, 'down',125)
cmp('thresh',.5)
pulse('time’,1e-6)
shatterPulse

## Slide 12: The Last Step -declareShatter
AMPpt4(t,AND(t,[wideValidThudPulse shatterPulse])) to declareShatter

## Slide 13: Comparison of Tanh and Log Results
Copyright 2020 Aspinity, Inc. Proprietary and Confidential, all rights reserved
Sophisticated timing constraints, i.e., shatter after thud, thud coincides with high frequency impulse, suppress thud after shatter
Log
141/148 67
129/148 59
Sophisticated timing constraints, i.e., shatter after thud, thud coincides with high frequency impulse, suppress thud after shatter
Tanh